UPCR-CPL3

Connector Plus

QIG

Table of Content

2. Connector References	- 3 -

3. Connector Pin Assignments	- 4 -

2. Connector References

Connector Plus Connector Index

| Reference Designation | Functional Description | Connector Type |
| --- | --- | --- |
| CN1 | Docking I | (TF)Board-Board Connector.100P.180D(F).SMD.Pitch=0.5mm.H=6.05mm.Panasonic.AXK5S00347YG |
| CN4 | Docking II | (TF)Board-Board Connector.100P.180D(F).SMD.Pitch=0.5mm.H=6.05mm.Panasonic.AXK5S00347YG |
| CN8 | WHL Function Connector | (TF)Wafer Box.10P.90D(M).SMD.1.0mm.PINREX.710-74-10TWR6 |
| CN2 | USB3.0 | (TF)USB3.0 Connector.Single Port.Type A.9P.90D(F).SMD.Trontek.930-00406-A91-22 |
| CN9 | M.2 Key B Slot | (TF)M.2 KEY-B SLOT.75P.90D(F).SMD.H=8.5mm.FOXCONN.2E0BC21-S85BB-7H |
| CN10 | SIM Slot | (TF).Micro SIM Card Socket.SMD.6P.90D.FEMALE.SHENG DA.CS-0025-06135.Push-Push type |
| LAN2 | LAN | (TF)RJ45.12P.90D(F).Notch down.W/LED(L-G:R-O/G).DIP.UDE.RC1-1Q00000D |
| LAN3 | LAN | (TF)RJ45.12P.90D(F).Notch down.W/LED(L-G:R-O/G).DIP.UDE.RC1-1Q00000D |
| LAN4 | LAN | (TF)RJ45.12P.90D(F).Notch down.W/LED(L-G:R-O/G).DIP.UDE.RC1-1Q00000D |
| CN11 | UART | (TF)Wafer Box.6P.180D.(M).SMD.1.0mm.w/ CAP.CATCH.1204-700-06SMR |
| CN13 | SPI | (TF)WAFER BOX.9P.180D(M).SMD.1.0mm.w/CAP.PINREX.710-H73-095WE1 |

TOP View：

Bottom View：

# 3.Connector Plus Connector Pin Assignments

  - CN1: Docking I

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | +V5A_CON | 2 | +V5A_CON |
| 3 | +V5A_CON | 4 | +V5A_CON |
| 5 | +V5A_CON | 6 | +V5A_CON |
| 7 | +V5A_CON | 8 | +V5A_CON |
| 9 | GND | 10 | GND |
| 11 | PLTRST_PNLBKLEN | 12 | LPSS_UART1_RTS |
| 13 | NC | 14 | LPSS_UART1_CTS |
| 15 | PM_SLP_S3#3V3 | 16 | LPSS_UART1_TXD |
| 17 | PCIE_CLKREQ3# | 18 | LPSS_UART1_RXD |
| 19 | NC | 20 | GND |
| 21 | GND | 22 | NC |
| 23 | SIO_SPI_0_TXD | 24 | NC |
| 25 | SIO_SPI_0_RXD | 26 | NC |
| 27 | SIO_SPI_0_CLK | 28 | NC |
| 29 | SIO_SPI_0_FS0 | 30 | NC |
| 31 | SIO_SPI_0_FS1 | 32 | ISH_GPIO_0 |
| 33 | GND | 34 | NC |
| 35 | NC | 36 | NC |
| 37 | NC | 38 | NC |
| 39 | NC | 40 | NC |
| 41 | NC | 42 | NC |
| 43 | GND | 44 | NC |
| 45 | NC | 46 | NC |
| 47 | NC | 48 | NC |
| 49 | NC | 50 | GND |
| 51 | NC | 52 | NC |
| 53 | GND | 54 | NC |
| 55 | NC | 56 | GND |
| 57 | NC | 58 | NC |
| 59 | GND | 60 | NC |
| 61 | NC | 62 | GND |
| 63 | NC | 64 | NC |
| 65 | GND | 66 | NC |
| 67 | NC | 68 | GND |
| 69 | NC | 70 | NC |
| 71 | GND | 72 | GND |
| 73 | I2C_SDA0 | 74 | NC |
| 75 | I2C_SCL0 | 76 | NC |
| 77 | GND | 78 | NC |
| 79 | NC | 80 | NC |
| 81 | NC | 82 | ISH_GPIO_11 |
| 83 | GND | 84 | ISH_GPIO_12 |
| 85 | NC | 86 | ISH_GPIO_13 |
| 87 | NC | 88 | ISH_GPIO_14 |
| 89 | GND | 90 | NC |
| 91 | NC | 92 | NC |
| 93 | NC | 94 | GND |
| 95 | NC | 96 | NC |
| 97 | NC | 98 | NC |
| 99 | NC | 100 | NC |

  - CN4: Docking II

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | +12V | 2 | +12V |
| 3 | +12V | 4 | +12V |
| 5 | +12V | 6 | +12V |
| 7 | +12V | 8 | +12V |
| 9 | NC | 10 | NC |
| 11 | NC | 12 | GND |
| 13 | NC | 14 | NC |
| 15 | NC | 16 | NC |
| 17 | GND | 18 | GND |
| 19 | NC | 20 | NC |
| 21 | NC | 22 | NC |
| 23 | GND | 24 | GND |
| 25 | NC | 26 | NC |
| 27 | NC | 28 | NC |
| 29 | GND | 30 | GND |
| 31 | PCIE_REFCLK0_P | 32 | PCIE_REFCLK1_P |
| 33 | PCIE_REFCLK0_N | 34 | PCIE_REFCLK1_N |
| 35 | GND | 36 | GND |
| 37 | PCIE_RXP0 | 38 | PCIE_RXP1 |
| 39 | PCIE_RXN0 | 40 | PCIE_RXN1 |
| 41 | GND | 42 | GND |
| 43 | PCIE_TXP0 | 44 | PCIE_TXP1 |
| 45 | PCIE_TXN0 | 46 | PCIE_TXN1 |
| 47 | GND | 48 | GND |
| 49 | PCIE_REFCLK2_P | 50 | PCIE_P3_USB3_P4_TXP |
| 51 | PCIE_REFCLK2_N | 52 | PCIE_P3_USB3_P4_TXN |
| 53 | GND | 54 | GND |
| 55 | PCIE_TXP2 | 56 | PCIE_P3_USB3_P4_RXP |
| 57 | PCIE_TXN2 | 58 | PCIE_P3_USB3_P4_RXN |
| 59 | GND | 60 | GND |
| 61 | PCIE_RXP2 | 62 | SATA_P1_USB3_P5_RXN |
| 63 | PCIE_RXN2 | 64 | SATA_P1_USB3_P5_RXP |
| 65 | GND | 66 | GND |
| 67 | PCIE_P4_USB3_P3_TXP | 68 | SATA_P1_USB3_P5_TXN |
| 69 | PCIE_P4_USB3_P3_TXN | 70 | SATA_P1_USB3_P5_TXP |
| 71 | GND | 72 | GND |
| 73 | PCIE_P4_USB3_P3_RXP | 74 | NC |
| 75 | PCIE_P4_USB3_P3_RXN | 76 | NC |
| 77 | GND | 78 | GND |
| 79 | USB2_DP3 | 80 | NC |
| 81 | USB2_DN3 | 82 | NC |
| 83 | GND | 84 | GND |
| 85 | USB2_DP4 | 86 | NC |
| 87 | USB2_DN4 | 88 | NC |
| 89 | GND | 90 | GND |
| 91 | NC | 92 | TP |
| 93 | PLTRST_PNLBKLEN | 94 | NC |
| 95 | PCIE_WAKE0_N | 96 | PCIE_CLKREQ0# |
| 97 | PCIE_WAKE1_N | 98 | PCIE_CLKREQ1# |
| 99 | PCIE_WAKE2_N | 100 | PCIE_CLKREQ2# |

  - CN8: WHL Function Connector

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | NC | 2 | I2C_SCL0 |
| 3 | I2C_SDA0 | 4 | GND |
| 5 | PM_SLP_S3#_3P3 | 6 | PCIE_CLKREQ3# |
| 7 | ISH_GPIO_12 | 8 | ISH_GPIO_13 |
| 9 | ISH_GPIO_14 | 10 | ISH_GPIO_11 |

  - CN2: USB 3.0 Type A Connector

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | +V5A_USB_1 | 2 | USB2_C_DN2 |
| 3 | USB2_C_DP2 | 4 | GND |
| 5 | USB3_RXN_CON_P2 | 6 | USB3_RXP_CON_P2 |
| 7 | GND | 8 | USB3_TXN_CON_P2 |
| 9 | USB3_TXP_CON_P2 |  |  |
| H1 | GND | H2 | GND |

  - CN9: M.2 Key B Slot with 3042/3052 for4G/5G Module

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | NC | 2 | +3.3V_NGFF_3052 |
| 3 | GND | 4 | +3.3V_NGFF_3052 |
| 5 | GND | 6 | FULL_CARD_POWER |
| 7 | 5G_DP | 8 | 5GPW_EN |
| 9 | 5G_DN | 10 | NC |
| 11 | GND | M.2 Key B |
| M.2 Key B |  |
|  | 20 | NC |
| 21 | NC | 22 | NC |
| 23 | 5G_Wake_Host | 24 | NC |
| 25 | NC | 26 | NC |
| 27 | GND | 28 | NC |
| 29 | PCIE_P3_USB3_P4_RXN_C | 30 | P_UIM_RST |
| 31 | PCIE_P3_USB3_P4_RXP_C | 32 | P_UIM_CLK |
| 33 | GND | 34 | P_UIM_DAT |
| 35 | PCIE_P3_USB3_P4_TXN_C | 36 | P_UIM_PWR |
| 37 | PCIE_P3_USB3_P4_TXP_C | 38 | PCIe_BOOT_Disable |
| 39 | GND | 40 | NC |
| 41 | PERn0_R- | 42 | NC |
| 43 | PERp0_R+ | 44 | NC |
| 45 | GND | 46 | NC |
| 47 | PETn0_T- | 48 | NC |
| 49 | PETp0_T+ | 50 | BUF_PLT_RST# |
| 51 | GND | 52 | PCIE_CLKREQ2# |
| 53 | CLK_PCIE_M2_3042_N | 54 | PCIE_WAKE2_N |
| 55 | CLK_PCIE_M2_3042_P | 56 | NC |
| 57 | GND | 58 | NC |
| 59 | NC | 60 | NC |
| 61 | NC | 62 | NC |
| 63 | NC | 64 | NC |
| 65 | NC | 66 | NC |
| 67 | WWAN_RESET | 68 | NC |
| 69 | M.2_3052_DET | 70 | +3.3V_NGFF_3052 |
| 71 | GND | 72 | +3.3V_NGFF_3052 |
| 73 | GND | 74 | +3.3V_NGFF_3052 |
| 75 | GND |  |  |

  - CN10: SIM Slot without detect (Push-Push Type)

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| C1 | P_UIM_PWRF | C2 | P_UIM_RSTC |
| C3 | P_UIM_CLKC |  |  |
| C5 | GND_UIM | C6 | NC |
| C7 | P_UIM_DATC |  |  |
| P1 | GND_UIM | P2 | GND_UIM |
| P3 | GND_UIM | P4 | GND_UIM |

  - LAN2: LAN2

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | LAN2_TMDI0+ | 2 | LAN2_TMDI0- |
| 3 | LAN2_TMDI1+ | 4 | LAN2_TMDI2+ |
| 5 | LAN2_TMDI2- | 6 | LAN2_TMDI1- |
| 7 | LAN2_TMDI3+ | 8 | LAN2_TMDI3- |
| 9 | LAN2_LED_1000# | 10 | LAN2_LED_100# |
| 11 | LAN2_ACTLEDN | 12 | LAN2_ACTLEDP |
| H1 | NC | H2 | NC |
| H3 | GND_CHASSIS_LAN | H4 | GND_CHASSIS_LAN |

  - LAN3: LAN3

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | LAN3_TMDI0+ | 2 | LAN3_TMDI0- |
| 3 | LAN3_TMDI1+ | 4 | LAN3_TMDI2+ |
| 5 | LAN3_TMDI2- | 6 | LAN3_TMDI1- |
| 7 | LAN3_TMDI3+ | 8 | LAN3_TMDI3- |
| 9 | LAN3_LED_1000# | 10 | LAN3_LED_100# |
| 11 | LAN3_ACTLEDN | 12 | LAN3_ACTLEDP |
| H1 | NC | H2 | NC |
| H3 | GND_CHASSIS_LAN | H4 | GND_CHASSIS_LAN |

  - LAN4: LAN4

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | LAN4_TMDI0+ | 2 | LAN4_TMDI0- |
| 3 | LAN4_TMDI1+ | 4 | LAN4_TMDI2+ |
| 5 | LAN4_TMDI2- | 6 | LAN4_TMDI1- |
| 7 | LAN4_TMDI3+ | 8 | LAN4_TMDI3- |
| 9 | LAN4_LED_1000# | 10 | LAN4_LED_100# |
| 11 | LAN4_ACTLEDN | 12 | LAN4_ACTLEDP |
| H1 | NC | H2 | NC |
| H3 | GND_CHASSIS_LAN | H4 | GND_CHASSIS_LAN |

  - CN11:UART

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | GND | 2 | CTSA |
| 3 | UART_VCC | 4 | TXA |
| 5 | RXA | 6 | RTSA |
| 7 | GND | 8 | GND |

  - CN12:SPI

| Pin | Signal Description | Pin | Signal Description |
| --- | --- | --- | --- |
| 1 | +V3.3S | 2 | +V5S |
| 3 | GND | 4 | CS0 |
| 5 | MISO | 6 | MOSI |
| 7 | CLK | 8 | INT_GPIO |
| 9 | CS1 | 10 | GND |
| 11 | GND |  |  |